## Slide 1: CTL Model Checking
Sayan Mitra
Verifying cyberphysical systems
mitras@illinois.edu

## Slide 2: This lecture: Requirements
Proof Certificate
System Model/Code & Property
Bug trace
Algorithm
or Method
System. A program/system for lane keeping control for vehicles
Requirement. The vehicle does not go outside the lane boundaries
Verification tool
counterexample. A particular environment situation (lane geometry, sensor failure, computer configuration) that makes the vehicle go outside lanes
A mathematical proof that establishes that for all allowed inputs and environments the vehicle stays with the lane
Model/assumptions: automaton, ODEs, hybrid automata
When can we build such a tool? How expensive is it? How well is it going to work? Under what assumptions?
Environment
/ Track
Perception
Controller program

## Slide 3: Requirements and safety in the real world
Requirements analysis: Set of tasks that ultimately lead to the determination and documentation of the design requirements that the product must meet:
E.g. “0 to 60 mph in 4 seconds on flat road”,
“Petrol car can emit no more than 60mg/km” EURO 6.
Safety standards: Provide guidelines and processes for developing safety-critical systems.
E.g. DO-178C standard is enforced by the FAA for certifying aviation software
ISO2626 is used for functional safety of cars
Standards for Advanced Autonomous and AI-enabled systems are being developed

## Slide 4: Requirements thus far: Invariants and stability
Models automaton, hybrid automaton
Requirements:
Given an unsafe set we can check whether to infer that
Asymptotic stability: Does as

## Slide 5
What about more general types of requirements, e.g.,
“Eventually the light turns red and prior to that the orange light blinks”
“After failures, eventually there is just one token in the system”
How to express and verify such properties?

## Slide 6: Outline
Temporal logics
  Computational Tree Logic (CTL)
CTL model checking for automata
  Setup
  CTL syntax and semantics
  Model checking algorithms
  Example
References: Model Checking, Second Edition, by Edmund M. Clarke, Jr., Orna Grumberg, Daniel Kroening, Doron Peled and Helmut Veith
Principles of Model Checking, by Christel Baier and Joost-Pieter Katoen

## Slide 7: Introduction to temporal logics
Temporal logics: Formal language for representing, and reasoning about, propositions qualified in terms of a sequence
Amir Pnueli received the ACM Turing Award (1996) for seminal work introducing temporal logic into computer science and for outstanding contributions to program verification.
Large follow-up literature, e.g., different temporal logics MTL, MITL, PCTL, ACTL, STL, applications in synthesis and monitoring
Notes: Bachelor's degree in mathematics from the Technion in Haifa, and Ph.D. in applied mathematics from the Weizmann Institute of Science. His thesis was on the topic of "Calculation of Tides in the Ocean".

## Slide 8: Setup: States are labeled
We have a set of atomic propositions (AP)
These are the properties that hold in each state, e.g., “light is green”, “has 2 tokens”
We have a labeling function that assigns to each state, a set of propositions that hold at that state

## Slide 9: Notations
Automata with state labels but no action labels
Executions (have no actions)
set of all executions

## Slide 10: Computational tree logic (CTL)
Unfolding the automaton
We get a tree
A CTL formula allows us to specify subsets of paths in this tree

## Slide 11: CTL quantifiers
Path quantifiers
E: Exists some path
A: All paths
Temporal operators
X: Next state
U: Until
F: Eventually
G: Globally (Always)

## Slide 12: CTL syntax
CTL syntax
where
Depth of formula: number of production rules used
Examples (depth)
AX; AX
Depth 3, 5, …
Non-examples
; path and state operators must alternate in CTL
: “no collision”
Invariance:
: “one token”
Stabilization:

## Slide 13: CTL semantics
Automaton and a CTL formula denotes that satisfies denotes that path (execution) satisfies is defined inductively as:
 | for
Automaton satisfies property: iff

## Slide 14: Universal CTL operators
can be used to derive other operators
All ten combinations can be expressed using

## Slide 15: Visualizing semantics

## Slide 16: Algorithm for deciding
Algorithm works by structural induction on the depth of the formula
Explicit state model checking
Compute the subset such that
Ifthen we can conclude

## Slide 17: Induction on depth of formula
Algorithm computes a function that labels each state with a CTL formula
Initially, for each
At iteration contains all sub-formulas of of depth that satisfies
At termination

## Slide 18: Structural induction on formula
Six cases to consider based on structure of
for some
if then
if then
if such that and then
[next slide]
[next slide]

## Slide 19
Let
for each
while
for each
for each
if then
Proposition. For any state iff .
Proposition. Finite therefore terminates and in steps.

## Slide 20
From we construct a new automaton such that
Claim. iff
with and is in a nontrivial Strongly Connected Components of the graph

## Slide 21
Claim. iff
and
with and is in a nontrivial SCC of the graph
Proof. Suppose
Consider any execution with Obviously, and so,
Since is finite can be written as where is finite and every state in repeats infinitely many times.
Let be the states in .
Consider any two and states in we observe that and therefore is a SCC.
Consider ( We construct a path such that and and visits some states infinitely often.

## Slide 22
Let
Let be the set of nontrivial SCCs of
for each
while
for each
for each such that
if then
Proposition. For any state iff .
Proposition. Finite therefore terminates and in steps.

## Slide 23: Putting it all together
 | for some
 | if then
 | if then
 | if such that and then
Explicit model checking algorithm input
Structural induction over CTL formula
Proposition. Overall complexity of CTL model checkign steps.

## Slide 24
1
!Start
!Close
!Heat
!Error
2
Start
!Close
!Heat
Error
3
! Start
Close
!Heat
!Error
4
!Start
Close
Heat
!Error
6
Start
Close
!Heat
!Error
5
Start
Close
!Heat
Error
7
Start
Close
Heat
!Error
Start oven
Open door
Close door
Open door
Start oven
Warmup
Start cooking
Reset
Open door
Close door

## Slide 25
1
!Start
!Close
!Heat
!Error
2
Start
!Close
!Heat
Error
3
! Start
Close
!Heat
!Error
4
!Start
Close
Heat
!Error
6
Start
Close
!Heat
!Error
5
Start
Close
!Heat
Error
7
Start
Close
Heat
!Error
Start oven
Open door
Close door
Open door
Start oven
Warmup
Start cooking
Reset
Open door
Close door
AG (Start -> AF Heat)

## Slide 26
1
!Start
!Close
!Heat
!Error
2
Start
!Close
!Heat
Error
3
! Start
Close
!Heat
!Error
4
!Start
Close
Heat
!Error
6
Start
Close
!Heat
!Error
5
Start
Close
!Heat
Error
7
Start
Close
Heat
!Error
Start oven
Open door
Close door
Open door
Start oven
Warmup
Start cooking
Reset
Open door
Close door
! EF (Start EG ! Heat)
! [True EU (Start EG ! Heat)]

## Slide 27
1
!Start
!Close
!Heat
!Error
2
Start
!Close
!Heat
Error
3
! Start
Close
!Heat
!Error
4
!Start
Close
Heat
!Error
6
Start
Close
!Heat
!Error
5
Start
Close
!Heat
Error
7
Start
Close
Heat
!Error
Start oven
Open door
Close door
Open door
Start oven
Warmup
Start cooking
Reset
Open door
Close door
! EF (Start EG ! Heat)
! [True EU (Start EG ! Heat)]

## Slide 28
1
!Start
!Close
!Heat
!Error
2
Start
!Close
!Heat
Error
3
! Start
Close
!Heat
!Error
4
!Start
Close
Heat
!Error
6
Start
Close
!Heat
!Error
5
Start
Close
!Heat
Error
7
Start
Close
Heat
!Error
Start oven
Open door
Close door
Open door
Start oven
Warmup
Start cooking
Reset
Open door
Close door
! EF (Start EG ! Heat)
Start, ! Heat
EG ! Heat
Nontrivial SCC of ! Heat

## Slide 29
1
!Start
!Close
!Heat
!Error
2
Start
!Close
!Heat
Error
3
! Start
Close
!Heat
!Error
4
!Start
Close
Heat
!Error
6
Start
Close
!Heat
!Error
5
Start
Close
!Heat
Error
7
Start
Close
Heat
!Error
Start oven
Open door
Close door
Open door
Start oven
Warmup
Start cooking
Reset
Open door
Close door
! EF (Start EG ! Heat)
Start, ! Heat
EG ! Heat
Set of states that can reach n
nontrivial SCC of ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
Start EG ! Heat

## Slide 30
1
!Start
!Close
!Heat
!Error
2
Start
!Close
!Heat
Error
3
! Start
Close
!Heat
!Error
4
!Start
Close
Heat
!Error
6
Start
Close
!Heat
!Error
5
Start
Close
!Heat
Error
7
Start
Close
Heat
!Error
Start oven
Open door
Close door
Open door
Start oven
Warmup
Start cooking
Reset
Open door
Close door
! EF (Start EG ! Heat)
Start, ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
Start EG ! Heat
Start EG ! Heat
Start EG ! Heat

## Slide 31
1
!Start
!Close
!Heat
!Error
2
Start
!Close
!Heat
Error
3
! Start
Close
!Heat
!Error
4
!Start
Close
Heat
!Error
6
Start
Close
!Heat
!Error
5
Start
Close
!Heat
Error
7
Start
Close
Heat
!Error
Start oven
Open door
Close door
Open door
Start oven
Warmup
Start cooking
Reset
Open door
Close door
! EF (Start EG ! Heat)
Start, ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
Start EG ! Heat
Start EG ! Heat
Start EG ! Heat
EF (Start EG ! Heat)

## Slide 32
1
!Start
!Close
!Heat
!Error
2
Start
!Close
!Heat
Error
3
! Start
Close
!Heat
!Error
4
!Start
Close
Heat
!Error
6
Start
Close
!Heat
!Error
5
Start
Close
!Heat
Error
7
Start
Close
Heat
!Error
Start oven
Open door
Close door
Open door
Start oven
Warmup
Start cooking
Reset
Open door
Close door
! EF (Start EG ! Heat)
Start, ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
Start EG ! Heat
Start EG ! Heat
Start EG ! Heat
EF (Start EG ! Heat)

## Slide 33
1
!Start
!Close
!Heat
!Error
2
Start
!Close
!Heat
Error
3
! Start
Close
!Heat
!Error
4
!Start
Close
Heat
!Error
6
Start
Close
!Heat
!Error
5
Start
Close
!Heat
Error
7
Start
Close
Heat
!Error
Start oven
Open door
Close door
Open door
Start oven
Warmup
Start cooking
Reset
Open door
Close door
! EF (Start EG ! Heat)
Start, ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
Start EG ! Heat
Start EG ! Heat
Start EG ! Heat
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
Set of states that can reach
Start EG ! Heat

## Slide 34
1
!Start
!Close
!Heat
!Error
2
Start
!Close
!Heat
Error
3
! Start
Close
!Heat
!Error
4
!Start
Close
Heat
!Error
6
Start
Close
!Heat
!Error
5
Start
Close
!Heat
Error
7
Start
Close
Heat
!Error
Start oven
Open door
Close door
Open door
Start oven
Warmup
Start cooking
Reset
Open door
Close door
! EF (Start EG ! Heat)
Start, ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
EG ! Heat
Start EG ! Heat
Start EG ! Heat
Start EG ! Heat
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
EF (Start EG ! Heat)
None of the states are labeled with
! EF (Start EG ! Heat)